## Slide 1
NYX Compute Infrastructure
Seetharaman Jayaraman, Xiaochun Yang, Howard Robinson
18th May 2016

## Slide 2
Rack 1
Rack 4,3,2
Rack 6,5
Rack 8,7
NYX Beamline Layout

## Slide 3
NYX Network Architecture
NYX Core Switch (10 Gig) in Rack 5 on the B hutch communicates with the NSLS II via two fiber channels on the Mezzanine.
Cat6 cable connects the Core Switch to switches (on dual copper CAT6, aggregated channel access) or devices in the 1, 2-4, 5-6 and 7-8 rack islands.
These switches can be configured to segregate traffic into sub domains.
Accelerator Timing fiber will be installed but not terminated.

## Slide 4
The EPICS IOC (Input/Output Controller) and EPICS archiver are co-located on a Linux computer in rack 5 on top of the D hutch.
Vacuum Controllers (RS-232) <-> Moxa (IP) <-> EPICS IOC and EPICS archive.
The EPS, Vacuum Controllers and Blu-Ice EPICS gateway communicate with the EPICS IOC via PVs (Process Variables).
EPS

## Slide 5
NYX IVU and Accelerator devices
The NYX IVU is controlled through an EPICS IOC on the Accelerator Network.
The Accelerator Network EPICS IOC PV’s for the IVU can be used through the Blu-Ice EPICS gateway to move the IVU Gap.